## Slide 1: Carbon Offsets: The Problems with the Emissions Reduction Fund Prof Andrew Macintosh The Australian National University

## Slide 2: Fundamental rule of carbon offsets
Carbon offsets are a high risk environmental instrument:
  Easy to get it wrong and issue low integrity credits because estimating abatement relative to a counterfactual is hard
  If credits have low integrity and they are used by polluters to offset emissions, it increases emissions
Consequence = only issue carbon offsets where high confidence they represent real and additional abatement

## Slide 3: What went wrong with the ERF?
Majority of credits being issued do not represent real and additional abatement
  Proximate cause = bad rules governing project eligibility and abatement estimation (bad methods) + poor interpretation/implementation by Clean Energy Regulator
  Root cause = poor governance and a lack of transparency

## Slide 4: Proximate Cause – bad methods and bad implementation

## Slide 5: The Big Three
ERF dominated by three project types:
  Avoided deforestation in western NSW = ~22% of issued ACCUs
  HIR = ~27% of issued ACCUs
  Landfill gas = ~27% of issued ACCUs
77% of the program comes from the big three
Major integrity problems with all three

## Slide 6: Avoided deforestation
Allows landholders in western New South Wales to get ACCUs for not clearing native forests
Based on assumption that landholders who applied for and received a specific type of clearing permit would use them within 15 years
Problem – clearing permits were substantially over-allocated, authorising clearing of substantially more forests than would ever have been cleared, particularly within 15 years
Risk = proponents would get ACCUs for not clearing forests they were never going to clear

## Slide 7: What does the evidence suggest? Required increase in historic clearing rate to clear credited forests in 15 years

## Slide 8: Human-induced Regeneration (HIR)
Allows landholders to earn ACCUs for regenerating native forests
Originally intended this would occur in areas that were previously cleared – a good idea
Most projects actually set up in semi-arid and arid rangeland areas that have not been comprehensively cleared – a bad idea
Most projects are trying to regenerate native forests in largely uncleared remnant native vegetation, purely by reducing grazing pressure from livestock and feral animals

## Slide 9
2013
2014
2015
2016
2017
2018
2019
2020
2021
ERF project areas
Native vegetation cover (NVIS)
Native vegetation
Cleared (MVG 25 and 29)
Sources: https://data.gov.au/data/dataset/erf_project_mapping
https://www.awe.gov.au/agriculture-land/land/native-vegetation/national-vegetation-information-system/data-products

## Slide 10: Problems with HIR
Two main integrity problems with HIR
Over-crediting: projects are being substantially over-credited because the model used to estimate tree growth assumes the areas have been substantially cleared (or >95% reduction in tree/shrub cover by another means)
Non-additionality: where trees are regrowing, it is mostly due to rainfall, not the reduction in grazing pressure (i.e. it is not additional)

## Slide 11: Over-crediting
Yr 1 (start): no mature trees/shrubs, biomass <5% of Max
Mid-age: even-aged (uniform) regeneration of trees and shrubs, with age of max growth 10-12.53 yrs
Max: maximum biomass site can contain with native vegetation
E.g. 160 tCO2 = made up of 16 25mx25m pixels, each with av max of 10 tCO2
Area-based model = estimates tree growth (biomass accumulation) in 1 ha of plantings or regenerating native forests

## Slide 12: What if there are already mature trees on the site?
Same principle – tree affected areas cover, say, 1,250 m2
Max biomass: was 160, now 160 – 5 – 5 – 5 – 5 = 140 tCO2
Project activity (planting or regeneration of trees) cannot occur successfully in areas affected by mature trees
Valid application of model requires either:
removal of areas with mature trees; or
reduction of max biomass in model

## Slide 13: What is happening?
For Environmental Plantings Method: proponents must exclude areas containing mature trees from credited areas
For HIR: proponents allowed to include areas with mature trees and no changes in model
Result = proponents of HIR projects are receiving ACCUs to grow trees that were already there when the projects started!

## Slide 14: HIR additionality
Most projects claiming they are regenerating native forests by reducing grazing pressure
Science suggests grazing has relatively limited impact on tree/shrub cover in rangeland areas
  Affects ground cover and biodiversity but limited impact on tree/shrub cover
  Certainly extremely rare (if not impossible) for grazing to reduce woody biomass by >95% over significant areas
Rain-drought cycle is the primary driver of tree/shrub cover changes

## Slide 15
Bourke (NSW)
Projects start

## Slide 16
Cobar (NSW)
Projects start

## Slide 17: Root Cause – bad governance and a lack of transparency

## Slide 18: Carbon offset markets are ‘special’
Normal market: buyer cares about quality, and sellers differentiate on basis of quality – means there is incentives to maintain quality
Carbon market: most buyers do not care about quality, sellers generally do not care about quality – means elevated importance of rule makers & regulators as guardians of integrity
Role of rule makers & regulators made more important by complexity – very hard for 3rd parties to evaluate and track integrity of offsets
Result = need strict separation of powers, radical transparency and processes to involve 3rd parties

## Slide 19: ERF governance structures
Strict separation of powers/roles: NO
  Clean Energy Regulation is the Rule maker, Regulator and Government buyer, and it staffs the Rule assessor
Transparency: NO
  Location of projects is published but not credited areas
  Offset reports – not published
  Audit reports – not published
  Abatement estimation assumptions – not published
3rd party involvement: NO
  3rd parties given limited or no access to rule making
  No third party appeals

## Slide 20: Conclusion
ERF is broken – bad rules, bad implementation and bad governance
New Government needs to intervene to ensure the ERF has integrity
The transition to integrity is going to be rough – vested interests are going to pay a price
There is a need for a price cap in the Safeguard Mechanism to shield polluters from the impacts of the transition to integrity